OPPO BDP-9x/10x Blu-ray Disc Player

Network Remote Control Protocol

OPPO BDP-9x/10x 可以通过网络来实现遥控的功能。该功能需要在BDP-9x/10x和网络设备（如 电脑，手机等）之间建立网络通信。BDP-9x/10x实现一个服务器的功能，负责广播消息，监听端口，等待客户端连接，接收客户端消息并处理。（下文BDP-9x/BDP-10x称为服务器端）。网络设备实现一个客户端的功能，负责接收并处理广播消息，同服务器端建立TCP连接，发送遥控命令。（下文具有此功能的网络设备称为客户端）。

客户端程序分为3个步骤实现：1,DISCOVER     2,CONNECT   3,COMMAND

- DISCOVER

服务器端运行后会每隔10秒钟发送广播消息，通知客户端服务器端已经在运行，并告之客户端需要跟服务器端建立连接的IP地址和端口号。

服务器广播消息的地址为239.255.255.251:7624

客户端运行后需要接收和处理服务器端的广播消息，并记忆服务器IP地址和端口号，和服务器建立连接后，如果再接收到该服务器的广播消息，应该丢弃。

服务器的广播消息格式：

Notify:OPPO Player Start

Server IP:(服务器的IP地址)

Server Port:(服务器监听的端口号)

例子：

Notify:OPPO Player Start

Server IP:192.168.0.2

Server Port:48360

- CONNECT

客户端需要利用从服务器广播消息中接收到的服务器的IP地址和监听的端口号，同服务器建立TCP连接。

- COMMAND

客户端同服务器端建立连接后，就可以发送遥控命令来实现对BDP-9x/BDP-10x的遥控操作。

命令格式：

<Command> = <Type of Command><sp><Command Code>

<Type of Command> =REMOTE

<sp> = space, ASCII 0x20

<Command Code> = <byte><byte><byte>

例如：

REMOTE EJT

实现开关仓的动作

遥控按键和Command Code对应关系如下：

| Command Code | Remote Key | Function |
| --- | --- | --- |
| SRC | SOURCE | Go to Home Menu to select media source |
| EJT | OPEN | Open/close the disc tray |
| PON | ON | Discrete on |
| POF | OFF | Discrete off |
| SYS | P/N | Switch output TV system: NSTC, PAL or MULTI(AUTO) |
| DIM | DIMMER | Dim front panel display |
| PUR | PURE AUDIO | Pure audio mode (no video) |
| VUP | VOL + | Increase volume |
| VDN | VOL - | Decrease volume |
| MUT | MUTE | Mute audio |
| NU1 | 1 | Numeric key 1 |
| NU2 | 2 | Numeric key 2 |
| NU3 | 3 | Numeric key 3 |
| NU4 | 4 | Numeric key 4 |
| NU5 | 5 | Numeric key 5 |
| NU6 | 6 | Numeric key 6 |
| NU7 | 7 | Numeric key 7 |
| NU8 | 8 | Numeric key 8 |
| NU9 | 9 | Numeric key 9 |
| NU0 | 0 | Numeric key 0 |
| CLR | CLEAR | Clear numeric input |
| GOT | GOTO | Play from a specified location |
| HOM | HOME | Go to Home Menu to select media source |
| PUP | PAGE UP | Show previous page |
| PDN | PAGE DOWN | Show next page |
| OSD | DISPLAY | Show/hide on-screen display |
| TTL | TOP MENU | Show BD top menu or DVD title menu |
| MNU | POP-UP MENU | Show BD pop-up menu or DVD menu |
| NUP | Up Arrow | Navigation |
| NLT | Left Arrow | Navigation |
| NRT | Right Arrow | Navigation |
| NDN | Down Arrow | Navigation |
| SEL | ENTER | Navigation |
| SET | SETUP | Enter the player setup menu |
| RET | RETURN | Return to the previous menu or mode |
| RED | RED | Function varies by content |
| GRN | GREEN | Function varies by content |
| BLU | BLUE | Function varies by content |
| YLW | YELLOW | Function varies by content |
| STP | STOP | Stop playback |
| PLA | PLAY | Start playback |
| PAU | PAUSE | Pause playback |
| PRE | PREV | Skip to previous |
| REV | REV | Fast reverse play |
| FWD | FWD | Fast forward play |
| NXT | NEXT | Skip to next |
| AUD | AUDIO | Change audio language or channel |
| SUB | SUBTITLE | Change subtitle language |
| ANG | ANGLE | Change camera angle |
| ZOM | ZOOM | Zoom in/out and adjust aspect ratio |
| SAP | SAP | Turn on/off Secondary Audio Program |
| ATB | AB REPLAY | Repeat play the selected section |
| RPT | REPEAT | Repeat play |
| PIP | PIP | Show/hide Picture-in-Picture |
| HDM | RESOLUTION | Switch output resolution |
| SUH | SUBTITLE (hold) | Press and hold the SUBTITLE key. This activates the subtitle shift feature |
| NOP |  | No operation. A dummy command. |
| POW | POWER | Toggle power STANDBY |